## Slide 1: Shape and Motion from Image Streams under Orthography: a Factorization Method
—— Group Member: Jieting Chen, Anbang Ye, Yicheng Sun, Jinbo Ci
From Tomasi & Kanade 1991a

## Slide 2: THE Factorization Method
Represent an image sequence as a 2F measurement matrix W, which is made up of the horizontal and vertical coordinates of P points tracked through F frames.
The 2F measurement matrix W can be factored into the product of two matrices R and S.
R —— 2F matrix that represents camera rotation
S —— 3 matrix that represents shape in a coordinate system attached to the object centroid.
U —— an FP matrix with one row per frame and one column per feature point
recording the horizontal feature coordinates
V —— an FP matrix with one row per frame and one column per feature point
recording the vertical feature coordinates
— with the assumption of orthographic graph

## Slide 3: Before Start: Find the corresponding P points
Select any four frames from all input images
Find the corresponding interesting points between the first frame with the other three frames
Find the common interesting points existing in all four frames
Use RANSAC Method to filtrate and get “good” interesting points

## Slide 4: the coordinates of feature points in world-centered or camera-centered coordinate?
With the perspective projection and a camera-centered representation of shape, the position of feature points is specified by their image coordinates and by their depths, defined as the distance between the camera center and the feature points, measured along the optical axis.
Unfortunately, although a camera-centered representation simplifies the equations for perspective projection, it makes shape estimation difficult, unstable, and noise sensitive.

## Slide 5
The orientation of the camera reference system corresponding to frame number f is determined by a pair of unit vectors if and jf pointing along the scanlines and the columns of the image respectively, and defined with respect to the world reference system. Under orthography, all projection rays are then parallel to the cross product of if and jf .
The image feature position of points onto frame f is given by the equation
=
=
where is the vector from the world origin to the origin of image frame f

## Slide 6: The FIRST step: compute the SVD
We have tracked P feature points over F frames in an image stream, record the result as
| f = 1, … F, p = 1, … P
write the horizontal feature coordinates into matrix U
write the vertical feature coordinates into matrix V
U —— an FP matrix with one row per frame and one column per feature point
recording the horizontal feature coordinates
V —— an FP matrix with one row per frame and one column per feature point
recording the vertical feature coordinates
– af
– bf
=
=
In order to be centered at the object centroid, the rows of the matrix U and V are registered by subtracting from each entry the mean of the entries in the same row.
This produces two new FP matrices and ]
The matrix = [], is called the registered measurement matrix
Notes: We have told how we get W before, in more detail…

## Slide 7: The second step: decompose the and calculate and
The matrix can be decomposed into a 2F matrix O1, a diagonal matrix , and a matrix O2, that is, operate SVD on and = O1 O2
O1 and O2 are orthograph matrices and is a diagonal matrix.
Suppose that we pay attention only to the first three columns of O1, the first submatrix of and the first three rows of O2.
Then and
We can write =
where the primes refer to the block partitioning in the picture.
However, the decomposition is not unique. In fact, if Q is any invertible matrix, the matrices Q and Q-1 are also a valid decomposition of .
Notes: Rank Theorem for Noisy Measurements:
The best possible shape and rotation estimate is obtained by considering only the three greatest singular values of , together with the corresponding left and right
eigenvectors.
Rank Theorem for Noisy Measurements:
The best possible shape and rotation estimate is obtained by considering only the three greatest singular values of 𝑊 ̃, together with the corresponding left and right
eigenvectors.

## Slide 8: The last two steps: calculate out R and S
The third step: Compute the matrix Q in equation (15) by imposing the metric constraints (equation (16)).
The fourth step: Compute the rotation matrix R and the shape matrix S as Q and Q-1
To calculate Q, we meet the problem and find out the method that …